## Slide 1: Alex Kelly GE Digital

## Slide 2
git clone https://github.com/pilotdeveloper/sensors_lab.git

## Slide 3: Please Pick Up
8 male to female jumper cables (different colors if possible).
12 male to male jumper cables (different colors if possible).
4 male to female jumper cables
Four pieces of electrical tape (1 x ~3 inches, 3 x 1 inch)
Four AA Batteries
10 µf electrolytic capacitor
1x NRF24L01+ Transceiver
4 tactical buttons
Ziploc bag with Arduino, Breadboard, Battery Holder, USB Cable

## Slide 4: Test your board
Open the Arduino IDE
Select Tools, Click Board -> Arduino Nano
Take note of the current devices under Tools -> Port (write down so you don’t select them later)
Plug your Arduino in, wait about 20 seconds, and then check under Tools -> Port.
      Windows – should show as a COM# device
      Mac Users – check the file called “mac_help.txt” in the repo.
Open the file helloworld/helloworld.ino and click the run button in Arduino

## Slide 5: hello_world.ino
Once you have hello_world running, you should be able to type a character and have your Arduino respond. If it doesn’t, please see us before we continue!

## Slide 6: What we’re building

## Slide 7: What we’re building

## Slide 8: Parts we’re using
NRF24L01+ Wireless Transceiver
Arduino Nano
10 µf Capacitor
Breadboard
Shoe Boxes

## Slide 9: The build
Start by connecting the Arduino and the NRF24L01+
NRF24L01+ | Arduino Pin
1 – GND | Ground
2 – VCC | 3v3
3 – CE | D9
4 – CSN | D10
5 – SCK | D13
6 – MOSI | D11
7 – MISO | D12
8 – IRQ | D8

## Slide 10: Capacitor
Bursting a signal requires a lot of energy – around 100 mA depending on the transmission strength. The Arduino Mano is not capable of handling this burst over 3.3v, so you have to add a capacitor to account for the voltage drops.
The capacitor must be connected across 3.3v and Ground on your NRF24L01. See photo in diagrams called “capacitor” for info on how to do this.
Be sure that the - - - (on the side of the capacitor) is on the ground side – you’ll short out the device if not!